## Slide 1: IGVC 2026 – FULL SUMMARY PRESENTATION
AutoNav • Self Drive • Design Challenge • Awards

## Slide 2: Competition Overview
33rd Annual Intelligent Ground Vehicle Competition
May 29 – June 1, 2026 • Oakland University, Rochester, Michigan
Events: AutoNav, Self Drive, Design Challenge

## Slide 3: Key Updates for 2026
Introduction of Top Performer Award (AutoNav + Self Drive)
Design reports must include autonomous subsystem analysis
Extended Self Drive testing windows
Continuation of the HBCU Award

## Slide 4: Team Requirements
Student-led teams with faculty supervision
Maximum of 3 vehicles per university
$500 registration fee per vehicle
50% discount for dual-event vehicle entries
International teams limited to 6 students + 2 faculty

## Slide 5: Vehicle Requirements
Fully autonomous unmanned ground vehicle
Dimensions: 3–7 ft length, 2–4 ft width, ≤ 6 ft height
Speed: 1–5 mph, hardware governed
Mandatory 20 lb payload
Mechanical and wireless E-stop required

## Slide 6: Qualification Requirements
All vehicles must pass qualification before competing
Includes speed test, lane following, obstacle avoidance
Vehicle safety systems must function flawlessly
Failure results in immediate disqualification

## Slide 7: AutoNav Challenge – Objective
Navigate a 500 ft outdoor obstacle course autonomously
Maintain lane position and required speed
Avoid static and dynamic obstacles
Scoring: adjusted time or adjusted distance

## Slide 8: AutoNav Course Details
Asphalt course with 10–20 ft lane widths
Obstacles: barrels, potholes, trees, cones
Minimum 1 mph required within first 44 ft
6-minute maximum run duration

## Slide 9: AutoNav Violations & Penalties
Leaving course: -10 ft + end of run
Obstacle crash/displacement: -10 ft + end of run
Sideswipe/touch: -5 ft
Careless driving: -5 ft
Payload loss ends run immediately

## Slide 10: Self Drive – Objective
Emulates high-level autonomous driving behaviors
Lane following, intersections, and turns
Stop sign recognition, pedestrian handling
Focus on perception, ML/DL, decision-making

## Slide 11: Self Drive Qualification Tests
Q1: Lane Keeping
Q2: Line Detection
Q3: Left Turn
Q4: Right Turn

## Slide 12: Self Drive – Functions Testing (16 Tests)
Pedestrian detection (static & moving)
Tire obstacle detection
Stop sign & fake sign classification
Parking maneuvers: pull-in, pull-out, parallel
Lane changes with obstacles
Curved path navigation
Pothole detection

## Slide 13: Self Drive – Full Course (21 Functions)
All functions executed sequentially in one run
Includes lane following, lane changes, turns
Pedestrians, obstacles, fake signs
Score: 2100 points total

## Slide 14: Design Challenge
Written report: 15–18 pages (strict format)
Oral presentation & Q&A
Vehicle technical inspection
Judged on requirements, design, KPIs, testing

## Slide 15: Design Report Requirements
Covers system architecture and subsystems
Mechanical, electrical, software, perception, logic
KPIs must be measurable and validated
Annual update required—no reuse

## Slide 16: Awards
AutoNav Awards
Self Drive Awards
Top Performer Award
Design Challenge Awards
Rookie of the Year
HBCU Flight Award
Grand Award